Post Office Protocol (POP2)
		      ...Faster than the US Snail!...


0.0 Introduction.

The Post Office Protocol (POP2), as defined in RFC 937, is a mail
protocol designed for use in networks containing workstations that
are normally turned off when they are not in use. In this environment it
is not possible for an SMTP mail server to deliver mail to these
workstations because they are not always available. The solution to
this problem is to designate a mailbox server that is available to
the network at all times and can accept SMTP mail for the workstations.
When a workstation comes on-line it uses POP2 to access the mail in its
mailbox(s) on the mailbox server. Although the networks discussed in
the RFC are wireline networks, such as Ethernet, notice the similarity
between this type of operation and the operation of an Amateur packet
radio network (in particular most of our tcpip networks).

The advantage to using a POP server at an area mail gateway, such as the
K6IYK Inter-LAN Gateway, is that when mail arrives at the gateway for
a station that may not be available, such as one that does not operate
24 hours a day, the gateway does not have to waste an SMTP connection
trying to establish a connection with that station. Instead it accepts
the mail and places it in the addressee's mailbox, just as if the
addressee was a normal user on the gateway system --  notice that this
is the same thing that is done by the AX25 BBSs. Hence, when the
addressee comes up on the network he/she collects his/her mail
from the mailbox. Note that although this process is, at present,
manually controlled, it is possible for a station to have a POP
daemon that becomes active when the station enters a network, or
upon user demand, automatically, and transparently, transfering new mail
from the mailbox server to the local mailbox at the station.


1.0 Starting and stopping the Server.

	The POP Server is controlled using the Start and Stop commands
that are already part of Net. To start the POP server include the
following command in your autoexec.net file:

			start pop

To stop the server issue the command:

			stop pop


2.0 Using the POP client.

	The POP client provides an automatic interface to the POP
Server that is totally transparent to the user; all that the user
needs to do is to set a few key parameters and the client will
take it from there. The following paragraphs describe the subcommands
that are accessed from the "pop" command.


2.1 mailbox command.

	The mailbox command allows the user to set the name of the
local mailbox that is to receive all of the mail received from the
mailbox server. Note that this mailbox name, like all DOS filenames,
is limited to eight (8) characters; it DOES NOT include the mail
directory path, which is the standard Net mail path /spool/mail. This
is a mandatory parameter that must be set inorder for the POP Client
for be able to work; failure to set the mailbox name will result in
a nasty message when the client is invoked.

2.2 mailhost command.

	The mailhost command allows the user to set the IP address of
the mailbox server that will be holding mail for the user. This is a
mandatory parameter that must be set inorder for the POP Client for be
able to work; failure to set the mailhost address will result in a nasty
message when the client is invoked.

2.3 kick command.

	The kick command causes the POP Client to be invoked.

2.4 timer command.

	The timer command allows the user to set the time interval
between successive invocations of the POP Client. Like the SMTP timer
command, the argument to this command is the time interval in seconds.
If the timer is not set then the POP Client will only run when it is
invoked with the kick command.

2.5 userdata command.

	The userdata command lets the user set the username and password
parameters required by the POP Client for access to the POP Server
on the mailbox server. Note that BOTH parameters MUST be entered when
this command is used. These are mandatory parameters that must be set
inorder for the POP Client for be able to work; failure to set the
username and password will result in a nasty message when the client is
invoked.

			**** N O T E ****

	Like the entries in the popuser file, the username and
	password entered with the userdata command ARE CASE
	SENSITIVE!

			**** N O T E ****


2.6 "Great, but how do I use it..."

	Using the POP Client is very simple; just add three lines
to your autoexec.net file to set the mailbox, mailhost, and userdata,
and then manually kick the client. For those of you who want to do
all of this without any manual intervention, just add a fourth line
that sets the timer value, and your mailbox on your mailbox server
will be checked and updated with new mail (providing it has arrived
at the mailbox server) at regular intervals. The following is an example
all that you would need to do to your autoexec.net file:

			.
			.
			.
		pop mailhost k6iyk
		pop mailbox mike
		pop userdata Mike SeCrEt_PaSsWoRd
			.
			.
			.
		# check mailbox every hour
		pop timer 3600
		# or manually do it when the system comes up
		pop kick
			.
			.
			.


Notice the similarity between the POP Client and the SMTP Client; the
only difference, outside of the POP Client state machine, in the way
that they operate is that only one POP Client session is allowed at a
time (i.e. you are only allowed one mailbox server!).


3.0 Errors.

	POP2, as specified in RFC 937, is a very simple protocol, with
a minimal amount of error handling. When an error is encountered
the connection is TERMINATED, period! Of course an error message is
sent, but otherwise you will have to re-establish a connection to
the server in order to continue. Normally this could be very frustrating,
but because of the limited functionality provided by POP2 it has not
seemed to be much of a problem in its typical environment (i.e.
"friendly user", for you non-unix types).

4.0 Installing the POP Server and POP Client in net/nos.

	Installation of the POP Server and POP Client into the net/nos source
is very simple, just follow the directions given in the following
paragraphs.

4.1 Source modifications.

	To include the POP Client and POP Server code into net/nos it is
necessary to add three files to the source, and to modify, or replace,
several others. In addition it is necessary to modify makefile and one
of the library description files. Once this has been done, all you
need to do is to run make to rebuild net/nos. The files that need to be
added/changed are

			for NET
			-------
			MAIN.C
			MAKEFILE.
			NETNAMES.RES
			NETUSER.H
			POP.H		*
			POPCLI.C        *
			POPSERV.C       *
			SESSION.H	(see note below)
			SESSION.C	(see note below)
			VERSION.C

			for NOS
			-------
			CLIENTS.TL
			COMMANDS.H
			CONFIG.C
			MAKEFILE.
			POP.H		*
			POPCLI.C        *
			POPSERV.C       *
			SERVERS.TL
			SOCKET.H
			VERSION.C

Those files marked with an asterisk (*) are new files, while the others
are existing files that have been modified to allow inclusion of the
POP code.

			**** N O T E ****

	The NET version of the POP code NO LONGER has a link to
	the SESSION.C module, so the original, unmodified version
	of SESSION.C and SESSION.H are used. For those of you who
	have trashed your original versions of those two files,
	they have been included in the NET release of the POP
	soource package.

			**** N O T E ****


4.2 Required Data files.

	This section describes the data files that are required by the
POP Server and the POP Client. Notice that they BOTH make use of the
user's mail file in /spool/mail, so exercise care in naming the mail
files on your system, least mail start disappearing for unknown reasons!!

4.2.1 POP Server data files.

	The POP Server requires one data file called "popusers."
to be created and placed in the system's root directory. This file,
as its name implies, contains the list of authorized users for the
system along with their passwords. Each line in the file describes
one user and is of the form

		<username> : <password> :

where <username> is the name of the user;
      <password> is this user's password.

Note that BOTH the username and password are CASE SENSITIVE, contrary
to the definition of the ftpusers file; also, the password is NOT
encrypted. It should also be clear that NEITHER the username NOR
the password may contain a COLON character. An  example segment of
this file is

			.
			.
			.
		 wa7dyx:sjkopqwZ34:
		 k6iyk:778GRCEqqrebr:
		 don-jacob:any_pAsSwOrD:
			.
			.
			.

	The user's mail is placed into the file
/spool/mail/<username>.txt, which is the same scheme used by
SMTP. Thus, the only other required file, the user's mail file, is
by default, already for use.

4.2.2 POP Client data files.

	The POP Client does not really require any data files, because
if it can't find the required file it makes it. Since the client
gathers mail from the mailbox server, it needs some place to store
the mail: the user's mailbox, as specified with the "pop mailbox"
command. The Client expects that the user's mailbox will be in the
/spool/mail directory, and only looks for the mailbox file in that
directory. Note, as with SMTP, all new mail is appended to the end of
the mailbox file.

	Of course the Client does not directly write to the user's
mailbox; instead it creates a file mbox.pop in the current directory
and places all of the mail it receives in that file, appending the
contents of the file to the end of the mailbox when all mail has been
collected from the mailbox server. Normally this file is deleted after
its contents have been trasnfered to the mailbox, however, if the
POP Client is unable to access the mailbox, for example it is locked
by SMTP, then mbox.pop will remain in existence. Any new mail gathered
by the POP Client will be appendedto the end of mbox.pop and eventually
the mailbox will become available and mbox.pop's contents will be
transfered to it.


5.0 Limitations.

There are several limitations in this release of the POP package. First,
it still does not support the FOLDer command, although it is included in
the source code, because of potential security problems; a future
release may include a solution to this problem, possibly like the
one used for FTP to limit the directories that a user can access.
Second, this release has only been tested on an IBM PC/AT (I'm not one
of those rich Unix gurus who can afford to have four or five different
types of computers laying around the house) and built using Turbo C,
although there should not be many problems in getting it to compile and
run under unix because that was where the initial development was done.
Third, the implementation of the userdata command does not appear to be
the best way to enter the username and password, so any comments on
a better approach would be appreciated.

6.0 POC

Direct any questions or comments regarding this package, and, of course,
any bug reports, to:

	Mike Stockett
	Jet Propulsion Laboratory
	4800 Oak Grove Drive
	Pasadena, CA 91109
	MS 514-205

	Packet --
		(AX25)  WA7DYX @ K6IYK
		(tcpip) mike@wa7dyx.ampr.org

	Vox --
		(818)397-7257 (W)
		(818)339-6011 (H)

7.0 Modification History

05/27/90   -  Allen Gwinn (N5CKP)    Modified for more current NOS.



APPENDIX A.  References.

[1]	RFC-937, Post Office Protocol - Version 2, M. Butler, et al,
	USC ISI, February 1985.


APPENDIX B.  Accessing the POP Server through its telnet port.

Stations without the POP Client installed in their Net software
may still access the POP Server and retrieve mail using telnet
to connect to port 109 on their mail server host machine. The following
paragraphs give a very brief and simple description of the basic
POP.

The Commands --

POP recognizes the following commands, which MUST BE in uppercase:

		.  HELO <username> <password>       initiate a session
						    for user <username>
						    with password
						    <password>;

		.  READ [<optional message number>] initiate a transaction
						    to read the next (or
						    the specified) message;

		.  RETR                             causes the message
						    selected to be
						    transmitted;

		.  ACKD				    acknowledges
						    successful receipt
						    of the message, and
						    tells the server to
						    DELETE it from the
						    user's mailbox;

		.  ACKS                             acknowledges
						    successful receipt
						    of the message, and
						    tells the server to
						    SAVE it in the user's
						    mailbox;

		.  NACK	                            indicates that the
						    message was not
						    successfully received;

		.  QUIT                             terminates the
						    session with the
						    server.

The Responses --

The set possible responses to the commands given above are limited and
not all of them will appear for each command, naturally. The full set
of responses for the POP Server is

		.  + 				indicates the
						successful completion
						of the specified
						operation; it may
						be followed by text;

		.  -				indicates failure of
						the specified operation,
						and may be followed by
						text;

		.  =				tells the length, in
						characters, of the
						message refered to by
						the command; this symbol
						is immediately followed
						by the length value, which
						may be followed by text;

		.  #				tells the number of messages
						in the folder or mailbox
						refered to by the command;
						this symbol is immediately
						followed by the count value,
						which may be followed by text.

The Protocol --

The following examples, purloined from RFC 937, show how the Post
Office Protocol is used to obtain mail from a POP server.

			   Example # 1

		Client				Server
		------				------
					 Wait for a connection
	Open the connection  -->
				   <--   + POP2 USC-ISIF.ARPA Server
	HELO Postel SECRET   -->
				   <--   #2 messages in your mailbox
	READ		     -->
				   <--   =537 characters in message 1
	RETR		     -->
				   <--	  [data of message 1]
	ACKD		     -->
				   <--	 =234 characters in message 2
	RETR		     -->
				   <--	 [data of message 2]
	ACKD		     -->
				   <--	 =0 no more messages
	QUIT		     -->
				   <--   + OK, bye, bye
	Close the connection -->   <--   Close the connection and
					 go back to start


			    Example # 2

		Client				Server
		------				------
					 Wait for a connection
	Open the connection  -->
				   <--   + POP2 USC-VAXA.ARPA server here
	HELO smith secret    -->
				   <--   #27 messages in your mailbox
	READ 27		     -->
				   <--   =10123 characters in that message
	RETR		     -->
				   <--	  [data of message 10123]
	ACKS		     -->
				   <--	 =0 no more messages
	QUIT		     -->
				   <--   + bye, call again sometime
	Close the connection -->   <--   Close the connection and
					 go back to start


			      Example # 3

		Client				Server
		------				------
					 Wait for a connection
	Open the connection  -->
				   <--   + POP2 USC-VAXA.ARPA server here
	HELO smith secret    -->
				   <--   #0 messages
	READ 		     -->
				   <--   Close the connection
	Close the connection -->
					 Go back to start


These examples show three of the many ways of using this protocol,
but the key thing to note is that the text messages that may
appear with the various response messages MAY VARY OR ABSENT.
Thus it is best to use a Client process to interface between the
user and the Server. Remember: an error will cause the connection
to be terminated!